## Slide 1
TECHZONE
RETAIL STORE
NETWORK PLAN

## Slide 2
BUSINESS OVERVIEW
TechZone is a three-story retail establishment specializing in selling the latest gadgets, accessories, and providing computer services. The store needs a robust and reliable network to support its point-of-sale (POS) systems, inventory management, customer Wi-Fi, and computer service operations.
The network will support all essential business activities, ensuring smooth operations and excellent customer service across its three floors.

## Slide 3
Stable wired connections
REQUIREMENTS
Segmentation of the network
IP surveillance
Wireless connectivity

## Slide 4
FLOOR PLAN
1ST FLOOR (Gadget Store)
  POS Systems - wired connections for all checkout counters.
  Staff Devices - wireless access for tablets and inventory management devices used by staff.
  Customer Wi-Fi - a dedicated wireless network for customer access.
  Surveillance Cameras - wired IP cameras for monitoring the shop area.

## Slide 5
FLOOR PLAN
2ND FLOOR (Accessories Store)
  POS Systems - wired connections for additional checkout counters.
  Sales Room - wired and wireless connections to handle customer inquiries, financial transactions, and access to inventory databases.
  Staff Devices - wireless access for staff to manage inventory and assist customers.
  Customer Wi-Fi - wireless network available for customers.
  Surveillance Cameras - wired IP cameras to monitor the accessories area.

## Slide 6
FLOOR PLAN
3RD FLOOR (Computer Services)
  Workstations - wired connections for service desks and computers used for repairs and customer consultations.
  Staff Personal Devices - wireless access for staff personal devices.
  Customer Wi-Fi - wireless network available for customers.
  Wireless Network - wireless access for technicians using tablets.
  Surveillance Cameras - wired connections for monitoring service areas.

## Slide 7
DEVICES | VLAN | NETWORK ADDRESS | IP ADDRESS RANGE | SUBNET MASK
2 POS System, Staff PCs, Wireless Router (Staff) | VLAN 10 | 192.168.10.0/24 | 192.168.10.10 – 192.168.10.50 | 255.255.255.0
Wireless Router (Customer), Customer Wi-Fi Devices | VLAN 40 | 192.168.40.0/24 | 192.168.40.10 - 192.168.40.50 | 255.255.255.0
CCTV Monitoring PC, Security Cameras (Wired) | VLAN 50 | 192.168.50.0/24 | 192.168.50.10 - 192.168.50.50 | 255.255.255.0
IP ADDRESS TABLE
1ST FLOOR

## Slide 8
DEVICES | VLAN | NETWORK ADDRESS | IP ADDRESS RANGE | SUBNET MASK
Sales PCs, Wireless Router (Staff), POS Systems | VLAN 20 | 192.168.20.0/24 | 192.168.20.10 - 192.168.20.50 | 255.255.255.0
Wireless Router (Customer), Customer Wi-Fi Devices | VLAN 40 | 192.168.40.0/24 | 192.168.40.10 - 192.168.40.50 | 255.255.255.0
CCTV Monitoring PC, Security Cameras (Wired) | VLAN 50 | 192.168.50.0/24 | 192.168.50.10 - 192.168.50.50 | 255.255.255.0
IP ADDRESS TABLE
2ND FLOOR

## Slide 9
DEVICES | VLAN | NETWORK ADDRESS | IP ADDRESS RANGE | SUBNET MASK
4 Workstation PCs (Computer Service), Wireless Router (Staff) | VLAN 30 | 192.168.30.0/24 | 192.168.30.10 - 192.168.30.50 | 255.255.255.0
Wireless Router (Customer), Customer Wi-Fi Devices | VLAN 40 | 192.168.40.0/24 | 192.168.40.10 - 192.168.40.50 | 255.255.255.0
CCTV Monitoring PC, Security Cameras (Wired) | VLAN 50 | 192.168.50.0/24 | 192.168.50.10 - 192.168.50.50 | 255.255.255.0
IP ADDRESS TABLE
3RD FLOOR

## Slide 10
NETWORK LAYOUT
Star Topology - each section (floor) has a switch (2960 24TT) that connects all the devices on that floor. The devices (PCs, routers, and security cameras) are connected to this central switch, making it a star configuration.
Hierarchical Structure - the switches on each floor may also be interconnected, potentially creating a larger hierarchical topology.

## Slide 11
THANK YOU!
GROUP 7
Viñas, Judah Paulo L. Bayrante, Reb G. Cordez, Roland Joseph P. Nodado, Mark Aratia, Jhoben S.
BSIT-3F